Drinking Water Quality and Compliance

VILLAGE OF ABBEY – Annual Notice to Consumers

Introduction

The Water Security Agency and the Ministry of Environment requires that at least once each year waterworks owners provide notification to consumers of the quality of water produced and supplied as well as information on the performance of the waterworks in submitting samples as required by a Minister’s Order or Permit to Operate a waterworks.  The following is a summary of the Village of Abbey water quality and sample submission compliance record for the Jan – Dec, 2021 time period.  This report was completed on July 6, 2022.  Readers should refer to Water Security Agency’s Municipal Drinking Water Quality Monitoring Guidelines, June 2015, EPB 502 for more information on minimum sample submission requirements and the meaning of type of sample.  Permit requirements for a specific waterworks may require more sampling than outlined in the department’s monitoring guidelines.  If consumers need more information on the nature and significance of specific water tests, for example, “what is the significance of Selenium in a water supply”, more detailed information is available from:  http://www.hc-sc.gc.ca/ewh-semt/pubs/water-eau/index_e.html .

## Water Quality Standards

# Bacteriological Quality

Regular Samples	Regular Samples	  # of Positive Regular

Parameter/Location	Limit			Required		Submitted	  Submitted (%)

Total Coliform 		0 Organisms/100 mL	__24_________	__27_________        ______0%__________

E. coli			0 Organisms/100 mL	__24_________	__27___________    ______0%__________

Background Bacteria	Less than 200/100 mL	__24_________	__27___________    ______0%__________

Water Disinfection –

Chlorine Residual in Distribution System for Test Results Submitted with Bacteriological Samples

Minimum	Total Chlorine	Free Chlorine	# Tests	# Tests	# Adequate

Parameter	Limit	Residual Range	Residual Range	Required	Submitted	Chlorine (%)

Chlorine	0.1 mg/L free OR

Residual	0.5 mg/L total	__0.61 – 1.49__	_0.07 – 0.68_	__24___	__27____	___100%______

Water Disinfection - Free Chlorine Residual for Water Entering Distribution System from Waterworks Records-From Water Treatment Plant Records

Test Level	# Tests                # Tests Not Meeting

Parameter	Limit (mg/L)	Range	Performed          Requirements

Free Chlorine Residual	at least 0.1	_0.1-0.98__	__365___       _____0 _____

=

A minimum of 0.1 milligrams per litre (mg/L) free chlorine residual is required for water entering the distribution system.  Tests are normally performed on a daily basis by the waterworks operator and are to be recorded in operation records.  This data includes the number of free chlorine residual tests performed, the overall range of free chlorine residual (highest and lowest recorded values) and the number of tests and percentage of results not meeting the minimum requirement of 0.1 mg/L free chlorine residual.

Turbidity – From Water Treatment Plant Records

Parameter	Limit	Test Level	# Tests Not Meeting	Maximum	# Tests           # Tests		# Tests

(NTU) 	Range	Requirements	Turbidity (NTU)	Required        Performed	Performed

Turbidity	__1___	0.21-.84	______________	__.84_____	__365___       ___365____	____________

Chemical – Health Category

All waterworks serving less than 5000 persons are required to submit water samples for SE’s Chemical Health category once every 2 years.  The Chemical Health category includes analysis for arsenic, barium, boron, cadmium, chromium, fluoride, lead, nitrate, selenium and uranium.

The last sample for Chemical Health analysis was submitted on August 25, 2021. Sample results indicated that the provincial drinking water quality standards were not exceeded.

Limit	Limit	Sample	# Samples

Parameter	MAC(mg/L)	IMAC (mg/L)	Result(s)	Exceeding Limit

Arsenic	0.010		_.0007____       ______ 0________   *  Results expressed

Barium	1.0		_.0144         	_______0________ 	  as average values

Boron	    5.0		_.4______	_______0________      for communities or

Bromate	0.01		_________	_______0________      waterworks that

Cadmium	0.005		_<.00015___	_______0________      fluoridate drinking

Chlorate	1.0		_________	_______0________      water supplies or

Chlorite	1.0		_________	_______0________      those with elevated

Chromium	0.05		  <.00019      	_______0________      concentrations of

Fluoride (avg*)	1.5		_.29_____	_______0________      fluoride or nitrates.

Lead	0.01		  .0001        	_______0________

Nitrate (avg.*)	45.0		  <0.2                	_______0________

Seleniuum	0.01		  <.00113_	_______0________

Uranium	0.02		   .0146      	_______0________

# General Chemical

Aesthetic 		Sample Results	# Samples  # Samples

### Parameter	Objectives * (mg/L)	(average)	Required     Submitted

Alkalinity	500	___498______	___1____ 	____1____

Bicarbonate	No Objective	___608______	___1____	____1____

Calcium	No Objective	__ 182______	___1____	____1____

Carbonate	No Objective	___0_______	___1____	____1____

Chloride	250	___6.7______ 	___1____	____1____

Conductivity	No Objective	___1667uS/cm	___1____	____1____

Hardness	800	___833_____	___1____	____1____

Magnesium	200	___1.23_______	___1____ 	____1____

PH	No Objective	___7.4________	___1____	____1____

Sodium	300	___106______	___1____	 ____1___

Sulphate	500	___510.6_____ 	___1____ 	 ____1___

Total dissolved

Solids                   1500	                         ___1514_____   ____1___      _____1___

All waterworks serving less than 5000 persons are required to submit water samples for SE’s General Chemical category once every two years if a ground water source and once per three months every second year if a surface water or blended surface/groundwater source.  The General Chemical category includes analysis for alkalinity, bicarbonate, calcium, carbonate, chloride, conductivity, hardness (as CaCO3), magnesium, sodium, sulphate and total dissolved solids.

The last sample for General Chemical analysis was required on 2021 and submitted on August 23, 2021. Samples exceeded provincial aesthetic objectives for the General Chemical category for the following parameters: total hardness, dissolved sulfates, total dissolved solids and manganese.

*Objectives apply to certain characteristics of or substances found in water for human consumptive or hygienic use.  The presence of these substances will affect the acceptance of water by consumers and/or interfere with the practice of supplying good quality water.  Compliance with drinking water aesthetic objectives is not mandatory as these objectives are in the range where they do not constitute a health hazard. The aesthetic objectives for several parameters (including hardness as CaCO3, magnesium, sodium and total dissolved solids) consider regional differences in drinking water sources and quality.

More information on water quality and sample submission performance may be obtained from:

Village of Abbey

Box 210

Abbey  SK   S0N 0A0

Phone: 306-689-2412

Fax:     306-689-2901

Email:  rm229@sasktel.net

June 2015         EPB 536D